## Slide 1
VALIDATION of H-SAF SNOW PRODUCTS
Alexander Toniazzo
Civil Protection Italy - Rome
Eumetrain EW 2021

## Slide 2
SUMMARY
Snow Products in H-SAF
Validation results, performances and limitations
Discussion and questions
H-SAF PT Meeting

## Slide 3
Snow Products in H-SAF
Legacy products over European area - operational
H10 Snow detection – Snow cover
H11 Snow status (wet/dry)
H12 Effective (Fractional) Snow Cover FSC
H13 Snow Water Equivalent SWE
Global and hemispherical products:
H34 and H35 new products (Snow det. and FSC) Pre-op
H31 and H32 ex L-Saf products (Snow det.) Op
H-SAF PT Meeting

## Slide 4
Ground Station Network
H-SAF PT Meeting
Weather stations
and snow detection: manual and automatic
SWE Stations
Country | Type | Number of Stations
Finland | Synoptic | 190
Turkey | Synoptic | 85
Italy | Snow/Avalanche | 264
Poland | Synoptic | 595
Germany | Synoptic | 1863
Belgium | Teleclim | 84
TOTAL |  | 3081

## Slide 5
Ground Station Network
H-SAF PT Meeting
Weather stations: manual and automatic
In some countries WMO Weather Stations are used, in other counties dedicated Snow Station Networks provide the data for validation.
Snow field in the Italian Alps with an Automatic Snow and Meteorological Station

## Slide 6
Ground Station Network
H-SAF PT Meeting
SWE Stations
For validating SWE high quality ground data is used.
The complete SPA System consists of two (2) SPA sensing bands with one installed horizontally 10 cm above the ground and the other installed at an angle (referred to as the sloping band), an impedance analyzer, an ultra-sonic snow depth sensor and mounting accessories to assure proper tension of the SPA bands. Each of the SPA bands sends frequencies into the snow pack and measures the complex impedance. Snow consists of ice, air and water. Each of these elements have different dielectric constants and when the band sends out the measuring frequencies it is able to read the returned value to determine the percentage of liquid water, ice and the remaining value as air.
Example of Ground Station in Turkey –
Snow Pack Analyser (SPA).

## Slide 7
H10 (H31) H32 and H34:
H-SAF PT Meeting
Validation methodology - Confusion matrix:
Hits n11, False alarms n01
Misses n10, Correct negatives n00
POD
FAR
Validation – Snow detection

## Slide 8
H10 in OR10 snow season 2019-20:
H-SAF PT Meeting
Statistical scores for H10 over mountainous and flat areas period 1.10.2019-31.5.2020
H-SAF Accuracy requirements for H10 in Flat/Forest areas |  |  |  | 
Product requirements |  |  |  | H10
Score | threshold | target | optimal | total
POD | 0.80 | 0.85 | 0.99 | 0.74
FAR | 0.20 | 0.15 | 0.05 | 0.27
H-SAF Accuracy requirements for H10 in Mountainous areas |  |  |  | 
Product requirements |  |  |  | H10
Score | threshold | target | optimal | total
POD | 0.60 | 0.70 | 0.99 | 0.70
FAR | 0.30 | 0.20 | 0.05 | 0.22
POD slightly out of spec for Flat/Forest areas, but fully compliant for Mountainous areas. Problems arise in H10 if snow is scarse and snow cover is not homogeneous in space and time, as was in winter 2019/20 in central Europe.
Validation results H10

## Slide 9
H10 in OR10 snow season 2019-20:
H-SAF PT Meeting
Statistical scores for H10 over mountainous and flat areas period 1.10.2019-31.5.2020
Validation has been performed over Belgium, Finland, Germany, Italy, Poland and Turkey.
The results are showed separately for flat and mountainous areas to provide complete error information on the product performances related to the orography.
flat area | Belgium | Finland | Germany | Poland | Average
numbers of obs | 2113 | 6910 | 1920 | 10331 | --
pod | 1.00 | 0.94 | 0.53 | 0.48 | 0.74
far | 0.21 | 0.22 | 0.31 | 0.35 | 0.27
csi | 0.79 | 0.74 | 0.43 | 0.38 | 0.59
pofd | 0.00 | 0.18 | 0.02 | 0.03 | 0.06
acc | 1.00 | 0.87 | 0.88 | 0.91 | 0.92
mountainous | Italy | Germany | Poland | Turkey | Average
numbers of obs | 1717 | 1464 | 974 | 8299 | --
pod | 0.55 | 0.76 | 0.57 | 0.91 | 0.70
far | 0.08 | 0.60 | 0.09 | 0.10 | 0.22
csi | 0.52 | 0.35 | 0.54 | 0.83 | 0.56
pofd | 0.10 | 0.24 | 0.22 | 0.50 | 0.27
acc | 0.67 | 0.56 | 0.62 | 0.84 | 0.67
Validation results H10

## Slide 10
H10 in OR8 snow season 2017-18
H-SAF PT Meeting
Statistical scores for H10 over mountainous and flat areas period 1.10.2017-31.5.2018
H-SAF Accuracy requirements for H10 in Flat/Forest areas |  |  |  | 
Product requirements |  |  |  | H10
Score | threshold | target | optimal | total
POD | 0.80 | 0.85 | 0.99 | 0.80
FAR | 0.20 | 0.15 | 0.05 | 0.14
H-SAF Accuracy requirements for H10 in Mountainous areas |  |  |  | 
Product requirements |  |  |  | H10
Score | threshold | target | optimal | total
POD | 0.60 | 0.70 | 0.99 | 0.75
FAR | 0.30 | 0.20 | 0.05 | 0.21
Validation results H10

## Slide 11
H-SAF PT Meeting
Problems arise in H10 if snow is scarse and snow cover is not homogeneous in space and time, as was in winter 2019/20 in central Europe.
H 34: full disk extension of H10 (to superseed H10)
validation strategy as in H10 is used, with ground data of the same countries.
For extra H-SAF areas a new validation scheme using Sentinel2 data with European and extra-European target areas is used (CIMA).
H32: hemispherical Snow Detection Product ex L-SAF
Same strategy as in H34, with ground data over Europe and Satellite data (CIMA) over extra-European areas. Results are very good (High resolution)
Validation H10 discussion

## Slide 12
H-SAF PT Meeting
H11 is validated with a temperature proxy – so no measure about wetness of snow is made.
In areas where there is a homogenous and stable snow cover product H11 can be considered reliable.
If a clear snow melting period - that is areas with snow cover going from dry to wet in H11 - is detected by the product, the data is valuable and usable for those hydrological applications, in which snow melting is an important factor.
H-SAF Accuracy requirements for H11 |  |  | 
Product requirements |  |  | 
Score | threshold | target | optimal
POD | 0.60 | 0.80 | 0.90
FAR | 0.20 | 0.10 | 0.05
Finland | ott-19 | nov-19 | dic-19 | gen-20 | feb-20 | mar-20 | apr-20 | mag-20 | Total
numbers of obs | 121 | 248 | 516 | 342 | 367 | 465 | 323 | 261 | 2643
pod | 0.90 | 0.99 | 1.00 | 1.00 | 0.93 | 0.81 | 0.74 | 0.24 | 0.87
far | 0.71 | 0.11 | 0.19 | 0.13 | 0.02 | 0.12 | 0.10 | 0.23 | 0.12
csi | 0.08 | 0.88 | 0.81 | 0.87 | 0.91 | 0.73 | 0.69 | 0.23 | 0.78
pofd | 0.69 | 1.00 | 1.00 | 1.00 | 0.53 | 0.65 | 0.49 | 0.10 | 0.63
acc | 0.99 | 0.88 | 0.81 | 0.87 | 0.91 | 0.74 | 0.71 | 0.51 | 0.79
Validation H11 Snow status (wet/dry)

## Slide 13
H11 is restricted to flat areas in Nordic countries. Validation only in in Finland, using same validation with an updated validation scheme.
In the mean, product H11 satisfies the requirements, with results of POD between target and optimal and FAR between threshold and target.
Validation group strongly recommends using product H11 in Nordic areas only during the winter and if snow cover is known to be sufficiently homogenous.
H-SAF PT Meeting
Validation H11 discussion

## Slide 14
Since 2018 new satellite-based data validation, using Sentinel 2 high resolution data (20 m) in selected target areas (mountain and flat areas).
H-SAF PT Meeting
Between target and optimal | Between threshold and target | Threshold exceeded by < 50 % | Threshold exceeded by ≥ 50 %
Scores | Aosta Valley | Pyrenees | Caucasus | Turkey
RMSE | 48.47 % | 49,36 % | 43,41 % | 19,88 %
H-SAF Accuracy requirements ESC Products |  |  | 
Score | threshold | target | optimal
Flat/Forested areas RMSE | 40% | 20% | 10%
Mountainous areas RMSE | 50% | 30% | 10%
Validation in 2018 OR8
Validation H12 Effective (Fractional) SC

## Slide 15
H 35: northern hemispheric extension of H12 (to superseed H12 in future )
Same validation strategy of H12 (CIMA)
H-SAF PT Meeting
In all areas H12 product meets the RMSE-based accuracy requirements.
CIMA study: threshold RMSE for mountainous areas not exceeded in any validation area, but values are just above threshold (very difficult mountainous terrain selected).
Turkey study: values are much better and are between target and optimal. In areas where snow cover is more homogeneous in space and in time, even in mountainous areas, H12 product has better performances.
Validation H12 and H35 discussion

## Slide 16
H13: operational Data from Poland, Finland, Turkey, Germany.
Validation 2019-20
H-SAF PT Meeting
H-SAF Accuracy requirements for H13 |  |  |  |  |  |  |  | 
Product requirements |  |  |  | RMSE (mm) |  |  |  | 
 | threshold | target | optimal | AVERAGE | Poland | Finland | Turkey | Germany
N. samples |  |  |  |  | 441 | 597 | 2848 | 1637
Mountainous | 45 mm | 25 mm | 15 mm | 39.2 mm |  |  | 39.2 mm | 
Flat Area | 40 mm | 20 mm | 10 mm | 23.5 mm | 9.5 mm | 36.7 mm |  | 24.2 mm
Area | Threshold | Target | Optimal
flat (RMSE) | 40 mm | 20 mm | 10 mm
mountain (RMSE) | 45 mm | 25 mm | 15 mm
Validation H13 Snow Water Eq.

## Slide 17
H-SAF PT Meeting
Detail over Finland and Turkey
General underestimation of SWE when values are larger than 150 mm.
Validation H13 details

## Slide 18
H-SAF PT Meeting
H13 satisfies the Product Requirements, with RMSE between threshold and target values.
Since the SWE product is developed for dry snow conditions, validation period is selected as December to March (or to April for Germany), only in Finland, where snow cover is more stable, the whole period October-May is evaluated.
Best performance are obtained in flat areas.
Turkish and Finnish studies: general underestimation of SWE when values are larger than 150 mm, slight overestimate below
Validation H13 discussion

## Slide 19
H-SAF PT Meeting
Snow Detection Products (Snow Cover) H10, H34, H32
  Best performances in flat areas, were snow cover is more homogeneous
  Problems arise if non homogeneous snow cover (space and time)
  Validation with ground data very difficult (filtering needed). Better performances with high resolution satellite data
Snow Status (Dry/Wet) H11: Validation suggest use only in Nordic areas (flat). Validation difficult if not impossible due to proxi data (temperature)
Fractional/Effective Snow Cover H12 and H35: Validation results good in flat areas, acceptable in mountainous areas, due to problems of resolution (complex terrain) and not homogeneous snow cover in mountains
SWE Products H13: Performances better in flat areas (RMSE 10-20 mm), in mountainous areas ( around 40 mm). Underestimate if more than 100 cm snow.
RECAP

## Slide 20
H-SAF PT Meeting
Thank You!